## Slide 1: Unit 2
CPU Pipeline

## Slide 2: Pipelined Y86 Implementation
Unit outline
  Motivation and basic concepts
  Initial Implementation
  Hazards
    Types of hazards
    Dealing with hazards by stalling
    Data hazards: forwarding to avoid stalling
    Control hazards: branch prediction
    Indirect jumps
  Performance analysis

## Slide 3: Design so Far
D
F
E
M
W
f.prPC | 
register file
main memory
CC

## Slide 5: Motivation and basic concepts
How instruction execution proceeds:
Sequential Y86 implementation
Instr 1:
Instr 2:
Instr 3:

## Slide 6: Motivation and basic concepts
Pipeline computation
  Divide the execution into modules (fetch, decode, ...)
    Modules are ordered along the flow of computation.
    One module's output is the input of the next module.
Turn each module into a pipeline stage.
  Add pipeline registers before every stage except the 1st.
  These store the inputs for that stage.
  Stages execute in parallel working on different instructions.
As we will see later this introduces new problems.

## Slide 7: Human Pipeline

## Slide 8: Sequencing a 3-Stage Pipeline
8
B
A
C
B
A
240
360
OP1
OP2
OP3




Time
120
Clock
Time = 239
R
e
g
Clock
Comb.
logic
A
R
e
g
Comb.
logic
B
R
e
g
Comb.
logic
C
100 ps
20 ps
100 ps
20 ps
100 ps
20 ps
Time = 241
R
e
g
Comb.
logic
A
R
e
g
Comb.
logic
B
R
e
g
Comb.
logic
C
100 ps
20 ps
100 ps
20 ps
100 ps
20 ps


Clock
Time = 300
R
e
g
R
e
g
R
e
g
100 ps
20 ps
100 ps
20 ps
100 ps
20 ps
Comb.
logic
A
Comb.
logic
B
Comb.
logic
C
Clock
Time = 359
R
e
g
Clock
Comb.
logic
A
R
e
g
Comb.
logic
B
R
e
g
Comb.
logic
C
100 ps
20 ps
100 ps
20 ps
100 ps
20 ps



## Slide 9: Sequencing a 3-Stage Pipeline
9
Time = 239
R
e
g
Clock
Comb.
logic
A
R
e
g
Comb.
logic
B
R
e
g
Comb.
logic
C
100 ps
20 ps
100 ps
20 ps
100 ps
20 ps
Time = 241
R
e
g
Comb.
logic
A
R
e
g
Comb.
logic
B
R
e
g
Comb.
logic
C
100 ps
20 ps
100 ps
20 ps
100 ps
20 ps


Clock

## Slide 10: Sequencing a 3-Stage Pipeline
10
Time = 300
R
e
g
R
e
g
R
e
g
100 ps
20 ps
100 ps
20 ps
100 ps
20 ps
Comb.
logic
A
Comb.
logic
B
Comb.
logic
C
Clock
Time = 359
R
e
g
Clock
Comb.
logic
A
R
e
g
Comb.
logic
B
R
e
g
Comb.
logic
C
100 ps
20 ps
100 ps
20 ps
100 ps
20 ps



## Slide 11: Pipeline Stages
How many stages should a pipeline have?
If it has too few stages...
  We are not exploiting the parallelism present in the program.
If it has too many...
  There is high overhead and complexity.
  The program may not have enough parallelism to use them well.

## Slide 12: Examples
MIPS processor (1985): first RISC processor, 5 stages.
Sparc, PowerPC processors: 9 pipeline stages.
Intel Pentium IV (late models): ____________
Intel Core i7 processor: _______________

## Slide 13: RISC vs CISC
Data Access
  RISC – only load and store operations access memory
  CISC – many different operations can access memory
Registers
  RISC – many general purpose registers
  CISC – few general purpose registers – some with special purpose
Addressing modes
  RISC – few & simple, so operation performance is easy to predict
  CISC – many so operation performance is unpredictable

## Slide 14: How do we measure processor efficiency?
Latency:
  How long it takes to execute one instruction from start to finish.
Throughput:
  The number of instructions we can execute per unit of time.
  This is the only meaningful measure for pipelined CPUs.

## Slide 15: Latency & Throughput
Sequential Implementation
Latency
Throughput

## Slide 16: Measuring Performance
Throughput
  the rate at which instructions leave the pipeline
  what is it here?______________
  in general? _________________
Latency
  total time it takes an instruction to be processed by entire pipeline
  what is it here? ______________
  in general? __________________
Pipeline Stages
Pipeline Overhead

## Slide 17: Pipelined Y86 Implementation
Unit outline
  Motivation and basic concepts
  Initial Implementation
  Hazards
    Types of hazards
    Dealing with hazards by stalling
    Data hazards: forwarding to avoid stalling
    Control hazards: branch prediction
    Indirect jumps
  Performance analysis

## Slide 18: Pipelined Computation
divide execution into modules along flow of computation
  classic RISC pipeline has five modules
  modules arranged in order along computation flow
  all inputs to a module must be computed by an earlier module in flow
turn modules into pipeline stages
  add pipeline registers between each stage
  registers store inputs for that stage
  each stage executes in parallel working on a different instruction
observe that
  a stage has less gate-propagation delay than overall circuit
  what determines clock rate? __________________________
  new instruction retrieved by FETCH on each cycle

## Slide 19: The RISC Pipeline
How many stages?
  enough to achieve sufficient parallelism
    must have enough parallelism in the program
  not too much to add undo overhead or complexity
What are they?
  divide instructions into stages that instruction completes in order
    e.g.: do A, then B, then C, then D, then D and then instruction is done
    then we can execute the stages in parallel on different instructions
lets look at rmmovq rA, D(rB), for example
  what are the parts?
  what order do they need to execute?

## Slide 20
rmmovq rA, D(rB) 40ABDDDDDDDDFFFFFFFF

## Slide 21: An Example Problem
What will each pipeline register contain when the last instruction in this sequence is entering the Fetch stage?
.pos 0x100
irmovq $1, %rax
irmovq $2, %rcx
irmovq $3, %rdx
irmovq $4, %rbx
irmovq $5, %rsi

## Slide 22: Data Flow Through Processor Stages
d.iCd | ➤
d.iFn | ➤
d.rA | 
d.rB | 
d.valC | ➤
d.valP | 
D
f.prPC | 
F
e.iCd | 
e.iFn | 
e.valC | 
e.srcA | 
e.srcB | 
e.dstE | 
e.dstM | 
e.valA | 
e.valB | 
E
➤
m.iCd | 
m.dstE | 
m.dstM | 
m.valA | 
m.valE | 
m.bch | 
M
w.iCd | 
w.dstE | 
w.dstM | 
m.valE | 
w.valM | 
W
register file
main memory
irmovq $1, %rax
irmovq $2, %rcx
irmovq $3, %rdx
irmovq $4, %rbx
irmovq $5, %rsi

## Slide 23: Data Flow Through Processor Stages
D
f.prPC | 
F
E
➤
M
W
register file
main memory
irmovq $1, %rax

## Slide 24: Data Flow Through Processor Stages
d.iCd | 
d.iFn | 
d.rA | 
d.rB | 
d.valC | 
d.valP | 
D
f.prPC | 
F
E
➤
M
W
register file
main memory
irmovq $1, %rax
irmovq $2, %rcx

## Slide 25: Data Flow Through Processor Stages
d.iCd | 
d.iFn | 
d.rA | 
d.rB | 
d.valC | 
d.valP | 
D
f.prPC | 
F
e.iCd | 
e.iFn | 
e.valC | 
e.srcA | 
e.srcB | 
e.dstE | 
e.dstM | 
e.valA | 
e.valB | 
E
➤
M
W
register file
main memory
irmovq $1, %rax
irmovq $2, %rcx
irmovq $3, %rdx

## Slide 26: Data Flow Through Processor Stages
d.iCd | 
d.iFn | 
d.rA | 
d.rB | 
d.valC | 
d.valP | 
D
f.prPC | 
F
e.iCd | 
e.iFn | 
e.valC | 
e.srcA | 
e.srcB | 
e.dstE | 
e.dstM | 
e.valA | 
e.valB | 
E
➤
m.iCd | 
m.dstE | 
m.dstM | 
m.valA | 
m.valE | 
m.bch | 
M
W
register file
main memory
irmovq $1, %rax
irmovq $2, %rcx
irmovq $3, %rdx
irmovq $4, %rbx

## Slide 27: Data Flow Through Processor Stages
d.iCd | 
d.iFn | 
d.rA | 
d.rB | 
d.valC | 
d.valP | 
D
f.prPC | 
F
e.iCd | 
e.iFn | 
e.valC | 
e.srcA | 
e.srcB | 
e.dstE | 
e.dstM | 
e.valA | 
e.valB | 
E
➤
m.iCd | 
m.dstE | 
m.dstM | 
m.valA | 
m.valE | 
m.bch | 
M
w.iCd | 
w.dstE | 
w.dstM | 
m.valE | 
w.valM | 
W
register file
main memory
irmovq $1, %rax
irmovq $2, %rcx
irmovq $3, %rdx
irmovq $4, %rbx
irmovq $5, %rsi

## Slide 28: Terminology
an instruction is in flight when
  it is executing in the pipeline
an instruction is retired when
  it exits the pipeline; i.e., it completes
on upcoming slides ...
  exploiting and expressing parallelism
  instruction-level parallelism
  instruction dependencies
  thread-level parallelism
  sequential consistency
  pipeline hazard, stall and bubble

## Slide 29: Ordering Instruction Execution
What we think now
  program we write specifies/determines order of instruction execution
What about the pipeline presents a problem?
  are pipelined instructions still executed in order?
  think about the register file ...
  what about conditional jumps ...
What really determines instruction execution order?

## Slide 30: Pipeline Considerations
Consider this code:
irmovq $5, %rax
addq %rax, %rdx
At what stage is irmovq in when addq needs %rax?
At what stage will %rax be updated?
At what stage is %rax extracted from the register file?

## Slide 31: Instruction-Level Parallelism
31
Pipeline requires some parallelism
  multiple in-flight instructions
  run partly at the same time
  may even run out-of-order
The program must have the same output as if instructions were executed sequentially.

## Slide 32: Dependencies Constrain Parallelism
A dependency means that the execution of 2 or more instructions has to proceed in strict time order to be able to produce the same output as if one instruction were completely executed before the next instruction is started.
If no dependency, execution order doesn’t matter
Compilers try to expose as much instruction-level parallelism as they can by separating dependent instructions and grouping them with others on which they don’t depend

## Slide 33: Dependencies
Example: how can we rewrite the following code to expose more parallelism?
addq %rax, %rbx
iaddq $5, %rbx
addq %rdx, %rcx
iaddq $9, %rcx
addq %rsi, %rdi
iaddq $3, %rdi

## Slide 34: Compilers & Instruction Parallelism
Compilers can reorder instructions to expose as much instruction-level parallelism as possible.
However they cannot know every detail of the processor's pipeline (e.g. later Pentium IV's had more stages than earlier ones).
So the pipeline must handle all dependencies correctly

## Slide 35: Dependency Types
Data dependencies
  This is involves dependencies between registers
Control dependencies
  This involves the flow of control (i.e. how the PC needs to be adjusted)

## Slide 36: Classifying Data Dependencies
if A and B are instructions, then A ≺ B means instruction B depends on instruction A.
  Causal: A ≺ B if B reads a value written by A.
  Output: A ≺ B if B writes to a location written by A.
  Alias (anti): A ≺ B if B writes to a location read by A.
Read “<“ as must happen before

## Slide 37: Control Dependencies
Whether a branch is taken or not taken (jmp, jxx, call, ret).
When an instruction writes to instruction memory (self-modifying code).

## Slide 38: Types of Data Dependency
a = 1;
b = 2;
a = 1;
a = 2;
a = 1;
b = a;
b = a;
a = 1;
(a) Causal dependency (c) anti (alias) dependency
(b) output dependency (d) no dependency
1.
2.
3.
4.

## Slide 39: Exercise Classify Examples
No dependency 3) anti-dependency
2) Casual dependency 4) output dependency
(a) irmovq $1, %rax rrmovq %rcx, %rax | (c) rrmovq %rax, %rcx irmovq $1, %rax
(b) irmovq $1, %rax rrmovq %rax, %rcx | (d) irmovq $1, %rax irmovq $2, %rcx

## Slide 40: Expressing vs Exploiting Parallelism
What does this mean?
expressing: its how the programmer tells the system that two pieces of code can execute in parallel
exploiting: is the system actually executing two pieces of code in parallel
How do you express parallelism in Java?
Is this mechanism useful for expressing ILP?

## Slide 41: Exploiting Instruction-Level Parallelism
The problem with instruction-level parallelism is:
Programming languages like C, C++ and Java are based on the sequential consistency model:
  The effect of executing the program must be the same as if instructions were executed one by one in the order they are written.
Programmers write code without thinking about parallelism
Example:
Can be rewritten as:
But compilers must find this on their own.

## Slide 42: Pipelined Y86 Implementation
Unit outline
Motivation and basic concepts
Initial implementation
Hazards
  Types of hazards
  Dealing with hazards by stalling
  Data hazards: using data forwarding to avoid stalling
  Control hazards: branch prediction
  Indirect jumps
Performance analysis.

## Slide 43: What is the problem here?
time
addq %rax, %rbx
F
D
E
M
W
F
D
E
M
W
F
D
E
M
W
F
D
E
M
W
F
D
E
M
W
addq %rax, %rcx
addq %rax, %rdx
irmovq $1, %rax
addq %rax, %rsi

## Slide 44: Hazard Definition
A pipeline hazard exists when the “normal” progression of instructions through the pipeline would violate a data or control dependency.
What can we do?
  Nothing?
Therefore:
One possible solution is:

## Slide 45: Pipeline Hazard
definition
  a pipeline hazard exists when the processor’s execution would violate a data or control dependency
what might we do
  can’t do nothing
    execution might produce erroneous results
  must detect
  we could stall
defns
  pipeline stall: holding an instruction in a pipeline stage for an extra cycle, always produces a bubble in the subsequent stage in the next cycle
  pipeline bubble: when a pipeline stage is forced to do nothing in order to avoid a hazard.
time
irmovq $1, %rax
addq %rax, %rbx
F
D
E
M
W
F
D
E
M
W
F
D
E
M
W
F
D
E
M
W
F
D
E
M
W
addq %rax, %rcx
addq %rax, %rdx

## Slide 46: Stalling
defns
  pipeline stall: hold an instruction in a pipeline stage for an extra cycle
    always produces a bubble in the subsequent stage in the next cycle
  pipeline bubble: when a pipeline stage is forced to do nothing in order to avoid a hazard. (result of a previous stall)
irmovq $1, %rax
addq %rax, %rbx
F
D
E
F
D
D
D
D
F
F
F
D
F
D
E
subq %rax, %rcx
xorq %rax, %rdx
M
W
M
W
E
M
E
time
F

## Slide 47: Stalling
defns
  pipeline stall: hold an instruction in a pipeline stage for an extra cycle
    always produces a bubble in the subsequent stage in the next cycle
  pipeline bubble: when a pipeline stage is forced to do nothing in order to avoid a hazard. (result of a previous stall)
irmovq $1, %rax
addq %rax, %rbx
F
D
E
F
D
D
D
D
F
F
F
D
F
D
E
subq %rax, %rcx
xorq %rax, %rdx
M
W
M
W
E
M
E
time
F

## Slide 48: Stalling
defns
  pipeline stall: hold an instruction in a pipeline stage for an extra cycle
    always produces a bubble in the subsequent stage in the next cycle
  pipeline bubble: when a pipeline stage is forced to do nothing in order to avoid a hazard. (result of a previous stall)
irmovq $1, %rax
addq %rax, %rbx
F
D
E
F
D
D
D
D
F
F
F
D
F
D
E
subq %rax, %rcx
xorq %rax, %rdx
M
W
M
W
E
M
E
time
F

## Slide 49: Stalling
defns
  pipeline stall: hold an instruction in a pipeline stage for an extra cycle
    always produces a bubble in the subsequent stage in the next cycle
  pipeline bubble: when a pipeline stage is forced to do nothing in order to avoid a hazard. (result of a previous stall)
irmovq $1, %rax
addq %rax, %rbx
F
D
E
F
D
D
D
D
F
F
F
D
F
D
E
subq %rax, %rcx
xorq %rax, %rdx
M
W
M
W
E
M
E
time
F

## Slide 50: Stalling
defns
  pipeline stall: hold an instruction in a pipeline stage for an extra cycle
    always produces a bubble in the subsequent stage in the next cycle
  pipeline bubble: when a pipeline stage is forced to do nothing in order to avoid a hazard. (result of a previous stall)
irmovq $1, %rax
addq %rax, %rbx
F
D
E
F
D
D
D
D
F
F
F
D
F
D
E
subq %rax, %rcx
xorq %rax, %rdx
M
W
M
W
E
M
E
time
F

## Slide 51: Stalling
defns
  pipeline stall: hold an instruction in a pipeline stage for an extra cycle
    always produces a bubble in the subsequent stage in the next cycle
  pipeline bubble: when a pipeline stage is forced to do nothing in order to avoid a hazard. (result of a previous stall)
irmovq $1, %rax
addq %rax, %rbx
F
D
E
F
D
D
D
D
F
F
F
D
F
D
E
subq %rax, %rcx
xorq %rax, %rdx
M
W
M
W
E
M
E
time
F

## Slide 52: Stalling
defns
  pipeline stall: hold an instruction in a pipeline stage for an extra cycle
    always produces a bubble in the subsequent stage in the next cycle
  pipeline bubble: when a pipeline stage is forced to do nothing in order to avoid a hazard. (result of a previous stall)
irmovq $1, %rax
addq %rax, %rbx
F
D
E
F
D
D
D
D
F
F
F
D
F
D
E
subq %rax, %rcx
xorq %rax, %rdx
M
W
M
W
E
M
E
time
F

## Slide 53: Stalling
defns
  pipeline stall: hold an instruction in a pipeline stage for an extra cycle
    always produces a bubble in the subsequent stage in the next cycle
  pipeline bubble: when a pipeline stage is forced to do nothing in order to avoid a hazard. (result of a previous stall)
irmovq $1, %rax
addq %rax, %rbx
F
D
E
F
D
D
D
D
F
F
F
D
F
D
E
subq %rax, %rcx
xorq %rax, %rdx
M
W
M
W
E
M
E
time
F

## Slide 54: Stalling
defns
  pipeline stall: hold an instruction in a pipeline stage for an extra cycle
    always produces a bubble in the subsequent stage in the next cycle
  pipeline bubble: when a pipeline stage is forced to do nothing in order to avoid a hazard. (result of a previous stall)
irmovq $1, %rax
addq %rax, %rbx
F
D
E
F
D
D
D
D
F
F
F
D
F
D
E
subq %rax, %rcx
xorq %rax, %rdx
M
W
M
W
E
M
E
time
F

## Slide 55: Stalling
defns
  pipeline stall: hold an instruction in a pipeline stage for an extra cycle
    always produces a bubble in the subsequent stage in the next cycle
  pipeline bubble: when a pipeline stage is forced to do nothing in order to avoid a hazard. (result of a previous stall)
irmovq $1, %rax
addq %rax, %rbx
F
D
E
F
D
D
D
D
F
F
F
D
F
D
E
subq %rax, %rcx
xorq %rax, %rdx
M
W
M
W
E
M
E
time
F

## Slide 56: Bubble
The term pipeline bubble denotes a pipeline stage that is forced to do nothing to avoid a hazard, because of a stall in a previous stage.
The bubble is an instruction that has been converted into a NOP

## Slide 57: Example
F
D
E
M
W
irmovq
?
?
?
?
addq
irmovq
?
?
?
subq
addq
irmovq
?
?
subq
addq
bubble
irmovq
?
subq
addq
bubble
bubble
irmovq
subq
addq
bubble
bubble
bubble
xorq
subq
addq
bubble
bubble
xorq
subq
addq
bubble
xorq
subq
addq

## Slide 58: Example
F
D
E
M
W
irmovq
?
?
?
?
addq
irmovq
?
?
?
subq
addq
irmovq
?
?
subq
addq
bubble
irmovq
?
subq
addq
bubble
bubble
irmovq
subq
addq
bubble
bubble
bubble
xorq
subq
addq
bubble
bubble
xorq
subq
addq
bubble
xorq
subq
addq

## Slide 59: Example
F
D
E
M
W
irmovq
?
?
?
?
addq
irmovq
?
?
?
subq
addq
irmovq
?
?
subq
addq
bubble
irmovq
?
subq
addq
bubble
bubble
irmovq
subq
addq
bubble
bubble
bubble
xorq
subq
addq
bubble
bubble
xorq
subq
addq
bubble
xorq
subq
addq

## Slide 60: Example
F
D
E
M
W
irmovq
?
?
?
?
addq
irmovq
?
?
?
subq
addq
irmovq
?
?
subq
addq
bubble
irmovq
?
subq
addq
bubble
bubble
irmovq
subq
addq
bubble
bubble
bubble
xorq
subq
addq
bubble
bubble
xorq
subq
addq
bubble
xorq
subq
addq

## Slide 61: Example
F
D
E
M
W
irmovq
?
?
?
?
addq
irmovq
?
?
?
subq
addq
irmovq
?
?
subq
addq
bubble
irmovq
?
subq
addq
bubble
bubble
irmovq
subq
addq
bubble
bubble
bubble
xorq
subq
addq
bubble
bubble
xorq
subq
addq
bubble
xorq
subq
addq

## Slide 62: Example
F
D
E
M
W
irmovq
?
?
?
?
addq
irmovq
?
?
?
subq
addq
irmovq
?
?
subq
addq
bubble
irmovq
?
subq
addq
bubble
bubble
irmovq
subq
addq
bubble
bubble
bubble
xorq
subq
addq
bubble
bubble
xorq
subq
addq
bubble
xorq
subq
addq

## Slide 63: Example
F
D
E
M
W
irmovq
?
?
?
?
addq
irmovq
?
?
?
subq
addq
irmovq
?
?
subq
addq
bubble
irmovq
?
subq
addq
bubble
bubble
irmovq
subq
addq
bubble
bubble
bubble
xorq
subq
addq
bubble
bubble
xorq
subq
addq
bubble
xorq
subq
addq

## Slide 64: Example
F
D
E
M
W
irmovq
?
?
?
?
addq
irmovq
?
?
?
subq
addq
irmovq
?
?
subq
addq
bubble
irmovq
?
subq
addq
bubble
bubble
irmovq
subq
addq
bubble
bubble
bubble
xorq
subq
addq
bubble
bubble
xorq
subq
addq
bubble
xorq
subq
addq

## Slide 65: Example
F
D
E
M
W
irmovq
?
?
?
?
addq
irmovq
?
?
?
subq
addq
irmovq
?
?
subq
addq
bubble
irmovq
?
subq
addq
bubble
bubble
irmovq
subq
addq
bubble
bubble
bubble
xorq
subq
addq
bubble
bubble
xorq
subq
addq
bubble
xorq
subq
addq

## Slide 66: Example
F
D
E
M
W
irmovq
?
?
?
?
addq
irmovq
?
?
?
subq
addq
irmovq
?
?
subq
addq
bubble
irmovq
?
subq
addq
bubble
bubble
irmovq
subq
addq
bubble
bubble
bubble
xorq
subq
addq
bubble
bubble
xorq
subq
addq
bubble
xorq
subq
addq

## Slide 67: Example
F | D | E | M | W
jne done |  |  |  | 
Addq %r9, %r10 rrmovq %r10, %rax |  |  |  | 

## Slide 68: What About Anti and Output Dependencies
They aren’t real dependencies provided instructions are executed in-order, which at this point we are assuming
Output is special case where first instruction’s output can be ignored
irmovq $1, %rax
irmovq $2, %rax
addq %rax, %rdx
irmovq $1, %rax
Causal
Output
Anti

## Slide 69: Types of Hazards
For our pipelined Y86 implementation:
Anti-dependency:
addq %rax, %rdx
irmovq $1, %rax
Output dependency:
addq %rax, %rdx
irmovq $1, %rdx
So the solution is:
Only issue if out
of order execution

## Slide 70: Doing Something Better than Stalling
Is important
  every stall creates a pipeline bubble
  every bubble results in a cycle when processor can’t retire an instruction
  retiring a bubble is of no value to program execution
What are the consequences of bubbles on throughput?
Ideas needed to deal with
  data dependencies
  control dependencies

## Slide 71: Y86 Pipeline Hazards
data hazards: only issue is
  causal hazards on register file, why?
  what not
    memory or condition codes?
control hazards
  conditional jump
  Return
  why not unconditional jump or call?

## Slide 72: Pipe–: Resolving Hazards by Stalling Summary
data hazards
  reading registers in decode that are written by instructions currently in execute, memory or write-back stages
  stall instruction in decode until writer is retired
  how many stall cycles? ______

## Slide 73: Control Hazards
  Conditional jump
  At what stage do we know which PC?
  At what stage is the PC needed?
  how many stall cycles? ______
Return
  The next PC is available at the end of?
  how many stall cycles? ______

## Slide 74: Example JNE
F | D | E | M | W
jne done | ? | ? | ? | ?
bubble | jne done | ? | ? | ?
bubble | bubble | jne done | ? | ?
rrmovq %r9,%rax | bubble | bubble | jne done | ?
addq %r8,%r9 | rrmovq %r9,%rax | bubble | bubble | jne done

## Slide 75: Example JNE
F | D | E | M | W
jne done | ? | ? | ? | ?
Bubble?? | jne done | ? | ? | ?
bubble | bubble | jne done | ? | ?
rrmovq %r9,%rax | bubble | bubble | jne done | ?
addq %r8,%r9 | rrmovq %r9,%rax | bubble | bubble | jne done

## Slide 76: Example JNE
F | D | E | M | W
jne done | ? | ? | ? | ?
Bubble?? | jne done | ? | ? | ?
Bubble?? | bubble | jne done | ? | ?
rrmovq %r9,%rax | bubble | bubble | jne done | ?
addq %r8,%r9 | rrmovq %r9,%rax | bubble | bubble | jne done

## Slide 77: Example JNE
F | D | E | M | W
jne done | ? | ? | ? | ?
Bubble??? | jne done | ? | ? | ?
Bubble??? | bubble | jne done | ? | ?
rrmovq %r9,%rax | bubble | bubble | jne done | ?
addq %r8,%r9 | rrmovq %r9,%rax | bubble | bubble | jne done

## Slide 78: Example JNE
F | D | E | M | W
jne done | ? | ? | ? | ?
Bubble??? | jne done | ? | ? | ?
Bubble??? | bubble | jne done | ? | ?
rrmovq %r9,%rax | bubble | bubble | jne done | ?
addq %r8,%r9 | rrmovq %r9,%rax | bubble | bubble | jne done

## Slide 79: Example ret
F | D | E | M | W
ret | ? | ? | ? | ?
Bubble??? | ret | ? | ? | ?
Bubble??? | bubble | ret | ? | ?
Bubble??? | bubble | bubble | ret | ?
popq %r9 | bubble | bubble | bubble | ret
popq %r10 | Poprq %9 | bubble | bubble | bubble

## Slide 80: Example ret
F | D | E | M | W
ret | ? | ? | ? | ?
Bubble??? | ret | ? | ? | ?
Bubble??? | bubble | ret | ? | ?
Bubble??? | bubble | bubble | ret | ?
popq %r9 | bubble | bubble | bubble | ret
popq %r10 | Poprq %9 | bubble | bubble | bubble

## Slide 81: Example ret
F | D | E | M | W
ret | ? | ? | ? | ?
Bubble??? | ret | ? | ? | ?
Bubble??? | bubble | ret | ? | ?
Bubble??? | bubble | bubble | ret | ?
popq %r9 | bubble | bubble | bubble | ret
popq %r10 | Poprq %9 | bubble | bubble | bubble

## Slide 82: Example ret
F | D | E | M | W
ret | ? | ? | ? | ?
Bubble??? | ret | ? | ? | ?
Bubble??? | bubble | ret | ? | ?
Bubble??? | bubble | bubble | ret | ?
popq %r9 | bubble | bubble | bubble | ret
popq %r10 | Poprq %9 | bubble | bubble | bubble

## Slide 83: Example ret
F | D | E | M | W
ret | ? | ? | ? | ?
Bubble??? | ret | ? | ? | ?
Bubble??? | bubble | ret | ? | ?
Bubble??? | bubble | bubble | ret | ?
popq %r9 | bubble | bubble | bubble | ret
popq %r10 | Poprq %9 | bubble | bubble | bubble

## Slide 84: Example ret
F | D | E | M | W
ret | ? | ? | ? | ?
Bubble??? | ret | ? | ? | ?
Bubble??? | bubble | ret | ? | ?
Bubble??? | bubble | bubble | ret | ?
popq %r9 | bubble | bubble | bubble | ret
popq %r10 | Poprq %9 | bubble | bubble | bubble

## Slide 85: Pipeline Control Unit
The pipeline-control module
  is a hardware component (circuit) separate from the 5 stages
  examines values across every stage
  decides whether stage should stall or bubble
85

## Slide 86: Dealing with hazards
Each stage register has a control input that determines what happens when the clock ticks:
  Normal: register's new value is the input value.
  Stall: register's new value is the same as its current value.
  Bubble: register's new value is the same as for NOP.

## Slide 87: Pipeline Control Unit
87

## Slide 88: In the Simulator
stage.stall/stage.bubble determine the control input for the stage registers:
In file Register.java:

## Slide 89: Pipelined Y86 Implementation
Unit outline
Motivation and basic concepts
Initial implementation
Hazards
  Types of hazards
  Dealing with hazards by stalling
  Data hazards: using data forwarding to avoid stalling
  Control hazards: branch prediction
  Indirect jumps
Performance analysis.

## Slide 90: Dealing with Causal Dependencies
may have to stall
  an instruction can’t read a value that the processor doesn’t know yet
but in most cases processor has computed value, it just hasn’t written it to the register file yet
so data forwarding will resolve hazard (in these cases)
  is mechanism that forwards values from later pipeline stages to earlier ones so that an instruction can read value before it is written back to register file

## Slide 91: Data Forwarding
In y86, at the end of what stage is output known by CPU?
  irmovq, addq, subq, andq, xorq, pushq, popq (rsp), call (rsp), ret (rsp)
  mrmovq, popl (target reg)
in y86, at the end of what stage is register value needed?

## Slide 92: Pipe (with forwarding)
92
to
  D
from
  W new value to register file
  M new value read from memory
  E new value from ALU
by
  sending value and name from all three stages back to forwarding logic in decode stage

## Slide 93
93

## Slide 94: Types of Y86 Data Hazards
register-register hazards
  rmmovq, irmovq, addq, subl, andl, xorl, pushq, popq (rsp), call (rsp), ret (rsp)
  forward to decode from execute, memory or write back
load-use hazards
  mrmovq, popq (target reg)
  stall use one cycle
  forward to decode from memory or write back
time
irmovq $1, %rax
addq %rax, %rbx
F
D
E
M
W
F
D
E
M
W
F
D
E
M
W
F
D
E
M
W
F
D
E
M
W
addq %rax, %rcx
addq %rax, %rdx
time
mrmovq (%esi), %rax
addq %rax, %rbx
F
D
E
M
W
F
D
E
M
W
F
D
E
M
W
F
D
E
M
W
F
D
E
M
W
addq %rax, %rcx
addq %rax, %rdx

## Slide 95: Register to Register Hazard with Data Forwarding
Instructions: irmovq, addq, subq, andq, xorq
    AND
pushq, popq, call, ret - all depend upon %rsp
Forward from _____ to _______
F
D
E
M
W
F
D
E
M
W
F
D
E
M
W
F
D
E
M
W
irmovq $10, %rax
addq %rax, %rbx
addq %rax, %rcx
addq %rax, %rdx
Time

## Slide 96: Load Use Hazard with Data Forwarding
Instructions: mrmovq, popq
Stall 1 cycle
Forward from _____ to _______
F
D
E
M
W
F
D
D
E
M
W
F
D
E
M
W
F
D
E
M
W
mrmovq (%esi), %rax
addq %rax, %rbx
addq %rax, %rcx
addq %rax, %rdx
Time
F

## Slide 97: Pipe (with forwarding)
97

## Slide 98: Forwarding implementation
In Decode – need to fix this part of the circuit:
D
rB
E
icode
ifun
valC
valA
valB
dstE
dstM
srcA
srcB
valC
valP
icode
ifun
rA
Register
file
A
B
M
E
dstE
dstM
srcA
srcB
d_srcB
d_srcA
d_rvalA
Sel+Fwd
A
Fwd
B
W_valM
W_dstE
E_dstE
d_rvalB
e_valE
M_dstE
M_valE
M_dstM
m_valM
W_dstM
W_valE
dstE
dstM
srcA
srcB
// read valA from register file
if (d.srcA.getValueProduced() != R_NONE)
d.valA.set (reg.get (d.srcA.getValueProduced()));
else
d.valA.set (0);

## Slide 99: Pipelined Y86 Implementation
Unit outline
Motivation and basic concepts
Initial implementation
Hazards
  Types of hazards
  Dealing with hazards by stalling
  Data hazards: using data forwarding to avoid stalling
  Control hazards: branch prediction
  Indirect jumps
Performance analysis.

## Slide 100: Control Dependencies
Do we have to stall?
Unconditional jumps and procedure calls
  Hazard? (e.g. jmp foo, call bar)
Conditional jumps
  Hazard? (e.g. jle foo)
  What is the problem?
  At what stage does the CPU know the answer?
Return
  Hazard? (e.g. ret)
  What is the problem?
  At what stage does the CPU know the answer?

## Slide 101: Jump Prediction
to resolve conditional-jump hazard
  jump is either taken or not, don’t know until jump is finished E
  don’t whether to use valP or valC for instruction following jump
guess at whether branch is taken or not
  guess that its either valP (not taken) or valC (taken)
  start these speculative instructions through pipeline
when jump reaches E we know if we guessed right
  speculative instructions have only gotten to D
  if guessed wrong, shoot down the instructions that should have executed
    turn them into bubbles, no-ops
result
  no bubble if guess right
  two bubbles if guess wrong
we will guess taken
  what is the right guess? more shortly ...
time
jle foo
F
D
E
M
W
F
D
E
M
W
F
D
E
M
W
F
D
E
M
W
F
D
E
M
W
time
jgt foo
F
D
E
M
W
F
D
E
M
W
F
D
E
M
W
F
D
E
M
W
F
D
E
M
W

## Slide 102: Branch Prediction
Problem:
  We won’t know whether or not to jump until end of Execute stage
  In the fetch stage (i.e. when setting the next PC) we don’t know if we should use valP (branch not taken) or valC (branch taken)
Idea:
  Guess whether or not branch taken
  Start speculative execution of instructions
  None will reach M or W stage before we know if the guess was wrong
Guess wrong:
  Shoot down all speculative instructions by turning into bubbles

## Slide 103: Branch Prediction
For conditional jumps:
  No bubble if guess right
  Two bubbles if guess wrong
F
D
E
M
W
F
D
E
M
W
D
E
M
W
F
D
E
M
W
0x100 jle $oxbadbeef
0xbadbeef addq %rax, %rbx
0xbadbeef + 2 addq %rax, %rcx
0x105 irmovq $0, %rax
Time
F

## Slide 104: Predicting the Next PC in Fetch Stage
104
unconditional jumps
  call and jmp
  predPC = valC, available in ?
conditional jumps
  know if branch taken in ?? (e_bch / M.bch)
  jump prediction in ??
    predict whether jump is taken
    predPC = valC (i.e., taken)
  misprediction control hazard
    handled by “Select PC” in F
    feedback from M
  no stall if prediction is correct
return from procedure call
  know target in M
    feedback from W to “Select PC” in F
  y86 stalls 3 cycles
    but, could use on-chip return-address stack
Instruction
memory
ALU
Data
memory
Select
PC
rB
Select
A
ALU
A
ALU
B
Mem.
control
Addr
read
write
Fetch
Decode
Execute
Memory
Write back
icode
A
f_PC
valE
valM
Bch
icode
valE
icode
ifun
valC
valA
valC
icode
ifun
rA
predPC
CC
E
M
W
F
D
PC
increment
Register
file
dstE
dstM
srcA
srcB
ALU
fun.
data out
data in
B
M
E
M_valA
W_valM
W_valE
M_valA
W_valM
d_rvalA
Predict
PC
dstE
dstM
valA
dstE
dstM
valB
dstE
dstM
srcA
srcB
valP
d_srcA
e_Bch
M_Bch

## Slide 105: Jump Prediction
Predict
  when conditional jump is in F
  F predicts taken, setting f.prPC to valC
If mis-predict, fetch from correct path
  when miss-predicted jump is in M
    i.e., M.bch == 0
  F ignores prPC; selects instruction at m.valP
If miss-predict, shootdown
  when mis-predicted jump is in E
  pipeline control sets D and E to bubble
private void fetch_PredictPC () {
f.prPC.set (valC or valP);
protected void fetch_SelectPC () {
// get correct PC for mispredicted jumps in M or ret in W
f.pc.set (?);
protected void pipelineHazardControl () {
// bubble D and E for mis-predicted jump and stall for ret
F
D
rB
M_icode
Predict
PC
valC
valP
icode
ifun
rA
Instruction
memory
PC
increment
predPC
Need
regids
Need
valC
Instr
valid
Align
Split
Bytes 1-5
Byte 0
Select
PC
M_Bch
M_valA
W_icode
W_valM
fetch has two sub-modules
protected void fetch () {
fetch_SelectPC ();
int pc = f.pc.getValueP...d()
...
fetch_PredictPC ();

## Slide 106: Exercise
Implement selectPC
protected void fetch_SelectPC () {
// get correct PC for mispredicted jumps in M or ret in W
f.pc.set (?);
F
D
rB
M_icode
Predict
PC
valC
valP
icode
ifun
rA
Instruction
memory
PC
increment
predPC
Need
regids
Need
valC
Instr
valid
Align
Split
Bytes 1-5
Byte 0
Select
PC
M_Bch
M_valA
W_icode
W_valM
protected void fetch () {
fetch_SelectPC ();
int pc = f.pc.getValueP...d()
...
fetch_PredictPC ();
fetch has two sub-modules

## Slide 107: Is it jump prediction or guessing?
Are jumps usually 50% likely to be taken, and 50% not?
  If so might as well just guess at random.
Consider how jumps are used in a program:
  loops:
    continue condition at bottom of loop is normally taken.
    exit condition at top of loop is normally not taken.
ifs:
  if testing for error condition, error handling code normally skipped.
  if testing for recursion base case, base case normally skipped.

## Slide 108: Observations
Most jumps tend to one way (taken or not taken for that line of code predominates)
Supported by empirical evidence
If we can figure this out we can improve a program’s performance

## Slide 109: What the compiler knows
In many cases the compiler can make a good prediction because:
  It creates the code
  For loops it knows if the jump means exit or continue
  Might be able to spot error test for ifs
  Only has the program text to make decisions on
  Cannot (usually) use dynamic information from execution

## Slide 110: What compiler wants from ISA
Conditional jumps to be predicted one way or the other.
ISA needs to state this explicitly so the compiler knows which way to adjust code
Complicated prediction rules are OK as long as it is specified

## Slide 111: Example of complex prediction
predict backward jumps are taken and forward jumps are not taken
  backward jumps (that just go a short distance) are almost always loop-continue jumps
  so they will be mostly taken
  forward jumps could be anything, so ISA might make this predict not taken to add flexibility
but, what’s most important is that the compiler know what the processor will do
Static
Jump
prediction

## Slide 112: Dynamic Jump Prediction
Sometimes the compiler can’t tell, but jump still has a strong tendency one way or another
  e.g., its hard for compilers to tell which if branch tends to be executed
Dynamic Jump Prediction is done by CPU Hardware
  this is a type of jump where the compiler does not know what will happen
  the hardware bases its prediction on the behaviour it observes of the jump

## Slide 113: Implementing
  CPU hardware maintains an on-chip cache of recent jump results
  when jump is in Execute stage (bch is computed) it updates this cache
  when jump is in Fetch state, use history as basis for prediction
(jump-address) => (was jump taken the last time it was executed?)
jumpCache.get (valP-9). set (bch)
f.prPC = jumpCache.get (valP-9)? valC : valP

## Slide 114: Even Better
Remember not just the last execution, but the last few by storing branch history as a sequence of bits with 1 indicating taken
  e.g., 1010 means the jump’s recent taken history was: no, yes, no yes
Use the count of the majority of bits as prediction
jumpCache.get (valP-9). set ((jumpCache.get (valP-9) << 1) | bch)
N = total # of bits used to store history (usually 4)
x = 0;
for (bits = jumpCache.get (valP-9).get(); bits!=0; bits >>> 1)
x += bits & 1;
f.prPC = (x > N/2)? valC : valP

## Slide 115: Even Better
Remember not just the last execution, but the last few by storing branch history as a sequence of bits with 1 indicating taken
  e.g., 1010 means the jump’s recent taken history was: no, yes, no yes
Use the count of the majority of bits as prediction
Try to observe a pattern

## Slide 116: Dynamic Prediction & Compiler
Compiler needs to know if jump prediction is used and how the decision is made
One option
  Have a set of branch instructions that use static prediction
  Second set that uses dynamic prediction
Why?

## Slide 117: The return Hazard
Problem
  Can’t predict what to put in F when ret moves to E
  Must read return address from memory but that doesn’t happen until M
Result
  leads to seeming inevitable 3 bubbles for each return
  returns are common, because procedures are small - a good idea for program readability, but with bad performance consequences

## Slide 118: Solution
Maintain a small stack of return addresses on the CPU Chip
  when call instruction in F
  when ret instruction in F
note that this stack is finite size and small, so return address may not be there
  in this case, we follow the old procedure and stall three times (i.e., iFn == 0)
returnCache.push (valP)
if (! returnCache.isEmpty ()) {
f.prPC = returnCache.pop ();
f.iFn = 1; // hack to tell pipelineHazardControl not to bubble

## Slide 119: Pipelined Y86 Implementation
Unit outline
Motivation and basic concepts
Initial implementation
Hazards
  Types of hazards
  Dealing with hazards by stalling
  Data hazards: using data forwarding to avoid stalling
  Control hazards: branch prediction
  Indirect jumps
Performance analysis.

## Slide 120: Indirect Jumps
Y86 doesn’t have these, but they are necessary and common
  Indirect jump: jmp D(%rax)
    PC  D + R[%rax]
  Double indirect jump: jmp *D(%rax)
    PC  M[D + R[%rax]]

## Slide 121: Problem
Unlike direct jumps, we do not know the target address in F
  for indirect we know it at the end of ??
  for double-indirect we know it at the end of ??
  Consequently, we cannot predict it in F, too many targets
This is really bad, why?
  virtually every procedure call in object-oriented language is double-indirect

## Slide 122: Polymorphic Dispatch
To generate code for the call object.method() (e.g. b.foo())
  object contains pointer to table with method addresses.
  Index into the table is determined by the method name.
  Assuming %rax is object address, D is method index:
  mrmovq (%rax), %rbx // %rbx is now table address
  call *D(%rbx) // jump to method address stored in table
class Base {
void foo () { ... }
void bar () { ... }
}
class Sub extends Base {
void foo () { ... }
}
void zot (Base b) {
b.foo ();
}

## Slide 123: B = new Base()
methodPtr
varB
varC
varA
Method1()
Method2()
Method1() {}
Method2() {}
B
Method Table for Base
methodPtr
varB
varC
varA
C

## Slide 124: B = new subBase()
methodPtr
varB
varC
varA
Method1()
Method2()
Method1() {}
Method2() {}
subB
Method Table for Base
Method1()
Method2()
subMethod2() {}

## Slide 125
void a1(void) {
printf("a1\n");
}
void a2(void) {
printf("a2\n");
}
int main(int argc, char **argv) {
void (*foo[2])(void);
foo[0] = a1; foo[1] = a2;
foo[0](); foo[1]();
}

## Slide 126: Prediction for Indirect Jumps
Key observation
  while compiler does not actually know the class of object, it knows only that the object implements the static type of the variable
  many variables tend to store objects of the same type over time
Key idea
  the hardware (or Java Virtual Machine) remembers object type and target address used the last time call was executed. If next call is to same type, it uses cached target address instead of reading it from memory.
Implementation
  maintain a cache of call instructions with address of procedure last called (ID a call instruction by its address)
    predict that call will call this same procedure again when the same call instruction is executed
This is bonus material. You will not be examined on this. You many ignore it.

## Slide 127: Summary of y86 pipeline hazards
127
in-order execution in pipeline
  focus only on dependency problems within one, in-order, pipeline
    but, modern processors = pipeline + add superscalar + out-of-order execution
data hazards (causal: read-after-write)
problems ⇒ erroneous computation
    register read in stage D
    but write in W
    non-problems
    memory, cc, and register output and anti
  solutions
    forward values across stages, stall if necessary (load/use)
    have new value in E or in M (for mrmovq and popl)
control hazards
  problem ⇒ pipeline bubble
    jxx target computed in E, ret in M
  solutions
    stall or delay slot plus forwarding
    or predict branch target in F
time
OP1
OP2
OP3
OP4
OP5
F
D
E
M
W
F
D
E
M
W
F
D
E
M
W
F
D
E
M
W
F
D
E
M
W
time
OP1
bubble
bubble
OP2
OP3
F
D
E
M
W
F
D
E
M
W
F
D
E
M
W
F
D
E
M
W
F
D
E
M
W

## Slide 128: Pipelined Y86 Implementation
Unit outline
Motivation and basic concepts
Initial implementation
Hazards
  Types of hazards
  Dealing with hazards by stalling
  Data hazards: using data forwarding to avoid stalling
  Control hazards: branch prediction
  Indirect jumps
Performance analysis.

## Slide 129: Performance Analysis
129
cycles per instruction (CPI)
  measures pipeline efficiency = 1/throughput
CPI = totalCycles / instructionRetiredCycles = 1 + lp + mp + rp
bubble penalties
  load/use lp = 1 bubble * probability of occurrence
  branch misprediction mp = 2 bubbles * probability of occurrence
  return rp = 3 bubbles * probability of occurrence

## Slide 130: Performance Analysis Example
130
Cause | Name | Instruction frequency | Condition frequency | Bubbles | Penalty
load/use | lp | 25% | 20% | 1 | ?
mispredict | mp | 20% | 40% | 2 | ?
return | rp | 2% | 100% | 3 | ?
total |  |  |  |  | ?
CPI = ?

## Slide 131: Limits to Pipeline Depth
Goal is improved throughput
  retired instructions / second
  (CPI * clock-period) -1
Are deeper pipelines better?
  Pros
  Cons

## Slide 132: Other Techniques
super-scalar
  Multiple pipelines that run in parallel
  Issue multiple instructions on each cycle
  Instructions execute in parallel and can even bypass each other
hyper-threading
  OS loads multiple runnable treads into CPU usually from same process
  CPU does fast switching among threads to use resources when one thread stalls
multi-core
  Multiple CPUs per chip, each pipelined, super-scalar etc.
  CPU’s execute independent threads from possibly different processes
  Typically have private L1 caches and a shared L2 cache
  Cores may be symmetric or not (i.e., with same capabilities or not)
    e.g., Intel Core Duo is symmetric and the IBM/Sony Cell processor is asymmetric

## Slide 133: Summary
ISA: y86 vs x86 (IA32)
  y86 is RISC-like
  x86 is CISC, converted to RISC micro ops in hardware
  e.g., addq %rax, (%rbx) is really 3 micro operations
y86 implementation: pipelined architecture
  divide execution into stages to improve throughput
  reduce cycle time; make more efficient use of transistors
  instruction-level parallelism
  dependencies and hazards
  data forwarding
  branch prediction
x86 implementation: y86 vs x86
  super-pipelined and superscalar
  redundant functional units
  out-of-order execution
  predict multiple branch paths at once
performance very workload sensitive