## Slide 1: Unit 5
Virtual Memory

## Slide 2: Virtual Memory Learning Goals
By the end of this unit, you should be able to:
  Explain why, despite the fact that Virtual Memory (VM) uses main memory as a cache for disk, VM tends to have significantly different organization and mechanisms from caches.
  Trace the translation of a virtual address to a physical address through a given translation lookaside buffer, page table, and cache to retrieve the physical address.

## Slide 3: An Overview
CPUs execute instructions
  Instructions and data are in main memory
Caches bring highly used data and instructions “closer” to the CPU to speedup access
Processes are collections of instructions and data
  Each process has: instructions, stack, heap, and data areas
Multiple processes reside in memory at once
How do we keep track of the memory all the processes are using?
415 will cover this and more!!
Shameless 415 plug

## Slide 4: Virtual Memory
Programs refer to memory addresses
  movl (%ecx),%eax
  Conceptually very large array of bytes
  Each byte has its own address
  Actually implemented with hierarchy of different memory types
  System provides address space private to particular “process”
Allocation: Compiler and run-time system
  Specify where different program objects should be stored
  Easier if all allocation for a program/process is within its own address space and the space has the same view/layout across all processes.
But why virtual memory?
Why not physical memory?
00∙∙∙∙∙∙0
FF∙∙∙∙∙∙F

## Slide 5: Problem 1: How Does Everything Fit?
64-bit addresses:
16 Exabyte
Physical main memory:
Few Gigabytes
?
And there are many processes ….
Not to scale
Program’s
address space
Actual amount of RAM
Notes: 5

## Slide 6: Problem 2: Memory Management
Physical main memory
What goes where?
stack
heap
.text
.data
…
Process 1
Process 2
Process 3
…
Process n
x
Each process has
Processes require differing amounts of code, stack, heap and data areas.
Notes: 6

## Slide 7: Problem 3: How To Protect
Physical main memory
Process i
Process j
Problem 4: How To Share?
Physical main memory
Process i
Process j
Notes: 7

## Slide 8: Solution: Level Of Indirection
Each process gets its own private memory space
Solves the previous problems
Physical memory
Virtual memory
Virtual memory
Process 1
Process n
mapping

## Slide 9: Address Spaces
Linear address space: Ordered set of contiguous non-negative integer addresses: {0, 1, 2, 3 … }
Virtual address space: Set of N = 2n virtual addresses {0, 1, 2, 3, …, N-1}
Physical address space: Set of M = 2m physical addresses {0, 1, 2, 3, …, M-1}
Clean distinction between data (bytes) and their attributes (addresses)
Every byte in main memory: one physical address, and one (or more) virtual address(es)
Each object (i.e. collection of bytes) can now have multiple addresses (This is a statement of fact, we will see how later.)
Notes: 9

## Slide 10: A System Using Physical Addressing
CPU
Used in “simple” systems like embedded microcontrollers in devices like cars, elevators, and digital picture frames
0:
1:
M-1:
Main memory
2:
3:
4:
5:
6:
7:
Physical address
(PA)
Data word
8:
...

## Slide 11: Virtual Memory
Unit 5
March 31

## Slide 12: A System Using Virtual Addressing
Used in all modern desktops, laptops, workstations
One of the great ideas in computer science
Cache is between MMU and main memory. Why?
0:
1:
M-1:
Main memory
MMU
2:
3:
4:
5:
6:
7:
Data word
8:
...
CPU
Virtual address
(VA)
CPU Chip
Cache
Physical address
(PA)

## Slide 13: Logical to Physical Address Translation
Code
Heap 
Stack 
Data
Physical Memory
MMU
Notes: 13

## Slide 14: 1- Why Virtual Memory (VM)?
Efficient use of limited main memory (RAM)
  Use RAM as a cache for the parts of a virtual address space
    some non-cached parts stored on disk
    some (unallocated) non-cached parts stored nowhere
  Keep only active areas of virtual address space (i.e. working set) in memory
    transfer data back and forth to disk as needed (Transfer is expensive)

## Slide 15: 2- Why Virtual Memory (VM)?
Simplifies memory management for programmers
  Each process gets the same full, private linear address space
Isolates address spaces
  One process can’t interfere with another’s memory since they operate in different address spaces
  User process cannot access privileged information since different sections of address spaces can have different permissions

## Slide 16: Memory Hierarchy: Core 2 Duo
Disk
Main Memory
L2 unified cache
L1
I-cache
L1
D-cache
CPU
Reg
2 B/cycle
8 B/cycle
16 B/cycle
1 B/30 cycles
Throughput:
Latency:
100 cycles
14 cycles
3 cycles
millions
~4 MB
32 KB
~4 GB
~500 GB
Not drawn to scale
L1/L2 cache: 64 B blocks
Miss penalty (latency): 30x
Miss penalty (latency): 10,000x
Notes: 16

## Slide 17: VM as a Tool for Caching
Virtual memory: array of N = 2n contiguous bytes
  think of the array (allocated part) as being stored on disk
Physical main memory (DRAM) = cache for allocated virtual memory
Blocks are called pages; size = 2p
PP 2m-p-1
Physical memory
Empty
Empty
Uncached
VP 0
VP 1
VP 2n-p-1
Virtual memory
Unallocated
Cached
Uncached
Unallocated
Cached
Uncached
PP 0
PP 1
Empty
Cached
0
2n-1
2m-1
0
Virtual pages (VP's)
(stored on disk, sort of)
Physical pages (PP's)
cached in DRAM
Disk

## Slide 18: DRAM Cache Organization
DRAM cache organization driven by the enormous miss penalty
  DRAM is about 10x slower than SRAM
  Disk is about 10,000x slower than DRAM
    For first byte, faster for next byte
Consequences
  Large page (block) size: typically 4-8 KB, sometimes 4 MB
  Fully associative
    Any VP can be placed in any PP
    Requires a “large” mapping function – different from CPU caches
  Highly sophisticated, computationally expensive replacement algorithms
    Too complicated and open-ended to be implemented in hardware
  Write-back rather than write-through

## Slide 19: Virtual Address -> Physical Address via Pages
Breakup the logical address ranges into pages (Same idea as a cache block)
Map each logical page of memory to a page frame of physical memory
Use a page table to maintain the mapping of virtual to physical addresses (page table is used by the MMU)
Each process has its own page table
Each time a process switch occurs there is a corresponding switch in the page table used by the MMU
Logical memory page is the same size as the physical memory page size
Notes: 19

## Slide 20: Virtual Memory
Unit 5
April 3

## Slide 21: Paging
An address reference is now composed of a page number and the offset into that page
MMU takes a virtual address and determines the page number to map to a page frame (physical page)
The offset is then appended to that page frame to produce the address of interest
Notes: 21

## Slide 22: Plan
Translate a virtual address to physical address
Page table structure
What happens on hits and misses
Multi-level page tables
TLB
Notes: 22

## Slide 23: Address Translation: Page Tables
A page table is an array of page table entries (PTEs) that maps virtual pages to physical pages. Here: 8 VPs
  Per-process kernel data structure in DRAM
null
null
Memory resident
page table
(DRAM)
Physical memory
(DRAM)
VP 7
VP 4
Virtual memory
(disk)
Valid
0
1
0
1
0
1
0
1
Physical page
number or
disk address
PTE 0
PTE 7
PP 0
VP 2
VP 1
PP 3
VP 1
VP 2
VP 4
VP 6
VP 7
VP 3

## Slide 24: Paging - High level view – so far
Each page is a fixed size (power of 2), typically 4K (Solaris 8K) but may be much a larger (4MB)
Location of frames does not correspond to order of pages (i.e. first logical page is not the first physical page)
Not all pages have corresponding frames (pages may be invalid)
Multiple pages may map to the same frame (shared memory)
The unit of swapping in or out is the page
Notes: 24

## Slide 25: MMU Role
Maintained by the kernel
Kept in regular main memory
Break a logical address into:
    Page number
    Offset into a page
Take the page number and look it up in a page table to get the frame's starting physical address
Append offset to the address to get the physical address to access
Hardware
Notes: 25

## Slide 26: Paging - Operation
MMU splits logical address into page number and offset
Offset is 0 to 212 – 1 (4095)
Page number range 0 to 220 – 1 (1,048,575)
20 bit page number
12 bit page offset
0
1
11
12
30
31
Notes: 26

## Slide 27: Examples
This implies that the page size is 212 or 4096 bytes
Suppose that 12 bit offset (virtual page offset VPO) and 20 bit virtual page index(VPI)
0x 12345678
Lookup 12345 in page table. Suppose it is 321, the physical address will be 0x321678
The page frame number

## Slide 28: Paging Problems
Have to keep track of many pages
Is there an efficient way to map from a page to a frame?
Is there an efficient way to provide memory protection?
Notes: 28
Ask how much information needs to be kept track of for a swapping system

## Slide 29: Single level page tables
Simplest solution is to use one page table per process
Table maps page of process's virtual (logical) memory space to physical frame
MMU uses the table to perform each look up
Page number corresponds to (indexes) page entry
Notes: 29

## Slide 30: Page table entry
Frame number
Valid/invalid bit
Reference bit
Dirty bit
Access bits
  read/write, code/data
Notes: 30

## Slide 31: Single level page tables
V
D
R
ACC
V
D
R
ACC
V
D
R
ACC
V
D
R
ACC
V
D
R
ACC
Current address-space
register
Notes: 31
The various colours above mean something
V -> valid page green yes, pink no
D -> dirty green yes, pink no
R - > referenced brown yes, clear no
Remark that there has to be one of these entries for every process

## Slide 32: Page Hit
Page hit: reference to VM word that is in physical memory
null
null
Memory resident
page table
(DRAM)
Physical memory
(DRAM)
VP 7
VP 4
Virtual memory
(disk)
Valid
0
1
0
1
0
1
0
1
Physical page
number or
disk address
PTE 0
PTE 7
PP 0
VP 2
VP 1
PP 3
VP 1
VP 2
VP 4
VP 6
VP 7
VP 3
Virtual address

## Slide 33: Page Miss
Page miss: reference to VM word that is not in physical memory
null
null
Memory resident
page table
(DRAM)
Physical memory
(DRAM)
VP 7
VP 4
Virtual memory
(disk)
Valid
0
1
0
1
0
1
0
1
Physical page
number or
disk address
PTE 0
PTE 7
PP 0
VP 2
VP 1
PP 3
VP 1
VP 2
VP 4
VP 6
VP 7
VP 3
Virtual address

## Slide 34: Handling Page Fault
Page miss causes page fault (an exception)
null
null
Memory resident
page table
(DRAM)
Physical memory
(DRAM)
VP 7
VP 4
Virtual memory
(disk)
Valid
0
1
0
1
0
1
0
1
Physical page
number or
disk address
PTE 0
PTE 7
PP 0
VP 2
VP 1
PP 3
VP 1
VP 2
VP 4
VP 6
VP 7
VP 3
Virtual address

## Slide 35: Handling Page Fault
Page miss causes page fault (an exception)
Page fault handler selects a victim to be evicted (here VP 4)
null
null
Memory resident
page table
(DRAM)
Physical memory
(DRAM)
VP 7
VP 4
Virtual memory
(disk)
Valid
0
1
0
1
0
1
0
1
Physical page
number or
disk address
PTE 0
PTE 7
PP 0
VP 2
VP 1
PP 3
VP 1
VP 2
VP 4
VP 6
VP 7
VP 3
Virtual address

## Slide 36: Handling Page Fault
Page miss causes page fault (an exception)
Page fault handler selects a victim to be evicted (here VP 4)
null
null
Memory resident
page table
(DRAM)
Physical memory
(DRAM)
VP 7
VP 3
Virtual memory
(disk)
Valid
0
1
1
0
0
1
0
1
Physical page
number or
disk address
PTE 0
PTE 7
PP 0
VP 2
VP 1
PP 3
VP 1
VP 2
VP 4
VP 6
VP 7
VP 3
Virtual address

## Slide 37: Handling Page Fault
Page miss causes page fault (an exception)
Page fault handler selects a victim to be evicted (here VP 4)
Offending instruction is restarted: page hit!
null
null
Memory resident
page table
(DRAM)
Physical memory
(DRAM)
VP 7
VP 3
Virtual memory
(disk)
Valid
0
1
1
0
0
1
0
1
Physical page
number or
disk address
PTE 0
PTE 7
PP 0
VP 2
VP 1
PP 3
VP 1
VP 2
VP 4
VP 6
VP 7
VP 3
Virtual address

## Slide 38: Address Translation With a Page Table
Virtual page number (VPN)
Virtual page offset (VPO)
Physical page number (PPN)
Physical page offset (PPO)
Virtual address
Physical address
Valid
Physical page number (PPN)
Page table base register
(PTBR)
Page table
Page table address
for process
Valid bit = 0:
page not in memory
(page fault)
Notes: 38

## Slide 39: Address Translation: Page Hit
1) Processor sends virtual address to MMU
2-3) MMU fetches PTE from page table in memory
4) MMU sends physical address to cache/memory
5) Cache/memory sends data word to processor

## Slide 40: Address Translation: Page Fault
1) Processor sends virtual address to MMU
2-3) MMU fetches PTE from page table in memory
4) Valid bit is zero, so MMU triggers page fault exception
5) Handler identifies victim (and, if dirty, pages it out to disk)
6) Handler pages in new page and updates PTE in memory
7) Handler returns to original process, restarting faulting instruction

## Slide 41: Integrating VM and Cache
VA: virtual address, PA: physical address, PTE: page table entry, PTEA = PTE address

## Slide 42: Paging - Benefits
Memory spaces no longer have to be contiguous in physical memory
Memory spaces can be large, millions of pages
Pages are all the same size so external memory fragmentation no longer occurs. Fragmentation in the swap space eliminated at the cost of keeping track of the pages
Need to swap out just as many pages as you need to make space, as opposed to the entire process or segment
Memory protection can be done on the level of pages
Memory can easily be shared by putting entries to the same physical pages into the page tables of different processes
Notes: 42
(still have internal fragmentation)

## Slide 43: Single Level PT Benefits
Simple data structure
Requires only one lookup to perform translation
Problem
  Table is proportional to size of memory space
  4 gigs / 4096 = 1 million entries * 8 bytes = 5-8 megabytes per process
We have a problem
Notes: 43
4 gigs / 4096 = 1 million entries * 8 bytes = 5-8 megabytes/process depending upon the size of the entry multiply that
by the number of processes and you have a problem if you have several hundred processes
But if we had only 24 bits like the IBM 370 machines then
16MB/4096 = 4096 * (5 or 8) = 20 – 32K much more manageable

## Slide 44: Multi-level tables
Instead of having a reference consist of a page number and offset
A reference consists of 2 or 3 indices and an offset
First index indexes first level table, which points to a second
Second index is then used to index second table
Eventually we find the frame number and perform the mapping
Don't have to store swaths of page mappings that are not used!
However, a translation now takes 2 or 3 main memory lookups!
That's expensive, 3 physical lookups for each logical memory address if we have 3 indexes!
Notes: 44
Point out that all these table are stored in main memory and accessing them has the same cost – how can this be sped up

## Slide 45: Virtual Memory
Unit 5
April 5

## Slide 46: Multi-level Tables - picture
V
D
R
ACC
V
D
R
ACC
V
D
R
ACC
V
D
R
ACC
V
D
R
ACC
V
D
R
ACC
V
D
R
ACC
V
D
R
ACC
V
D
R
ACC
V
D
R
ACC
Current address-space
register
V
V
V
V
V
12 bit page offset
0
1
11
12
30
31
21
22
10 bit table 1
10 bit table 2
Notes: 46
2^10 = 1024

## Slide 47: Speeding up address translation
Observation: Most address references are localized
Cache the translations
The Translation Lookaside Buffer (TLB) does this
It's associative memory that caches the page translations
Some TLB's can be loaded and saved as part of a process context switch
Notes: 47

## Slide 48: Updated MMU Operation
MMU
Logical Address
Check TLB
Cache
Check Page
Tables
TLB
PT 1
PT2
Update TLB
Cache
Physical Address
Notes: 48

## Slide 49: Updated MMU operation
Logical address is presented to the MMU
TLB is checked to see if there is a logical to physical address mapping present
  In parallel, start address lookup in page tables
If a mapping is found use mapping, stop PT lookup
If a miss wait for PT lookup to complete
  Store new logical to physical mapping in TLB
Have physical address at this point
For the TLB to be really useful, try to get a hit rate of greater than 95%.
Notes: 49

## Slide 50: TLB Miss
A TLB miss incurs an additional memory access (the PTE) Fortunately, TLB misses are rare. Why?
In parallel

## Slide 51: TLB Hit
A TLB hit eliminates a memory access
PTEA
In parallel
Cancelled on hit

## Slide 52: TLB Observations
The more TLB entries then:
  More translations can be held
  Higher the hit rates (i.e. fewer full lookups required)
  Result - faster overall operation
However
  Hardware for the TLBs is expensive (chip real estate, delays)
  Loading and unloading the TLB is expensive (time wise)
  Can a larger TLB improve the hit rate enough to matter?
Notes: 52
Talk about cost hit rate tradeoffs

## Slide 53: Why does it work? Locality
Virtual memory works because of locality
At any point in time, programs tend to access a set of active virtual pages called the working set
  Programs with better temporal locality will have smaller working sets
If (working set size < allocated main memory size)
  Good performance for one process after compulsory misses
If ( SUM(working set sizes) > main memory size )
  Thrashing: Performance meltdown where pages are swapped (copied) in and out continuously

## Slide 54: Page Replacement
The policy that selects the page frame to remove when space is needed
Poor page replacement algorithm can have a huge impact on the system performance
How do you decide what page to page out?
Notes: 54

## Slide 55: Replacement Policy
Optimal: This is the theoretical best possible choice
  The page to remove is the one that will not be used for the longest time (To implement this we would need to be able to predict the future)
Idea: Based on the idea of temporal locality, if a page hasn’t been used recently it is unlikely to be used and therefore a good candidate for eviction.
Notes: 55

## Slide 56: LRU approx:
Use page table reference bit
At a fixed interval shift reference bit into high bit of a counter for that page (counter is a history of the intervals each page was referenced in)
Page with smallest number is LRU (approximately)
  If all 1s then used in every scan interval, if all 0s then never used
Notes: 56
Bit shifted in is 0

## Slide 57: What problems can we solve with virtual memory?

## Slide 58: VM as a Tool for Memory Management
Key idea: each process has its own virtual address space
  It can view memory as a simple linear array
  Mapping function scatters addresses through physical memory
    Well chosen mappings simplify memory allocation and management
Virtual Address Space for Process 1:
Physical
Address
Space (DRAM)
0
N-1
(e.g., read-only
library code)
Virtual Address Space for Process 2:
VP 1
VP 2
...
0
N-1
VP 1
VP 2
...
PP 2
PP 4
PP 6
PP 8
...
0
M-1
Address
translation
NOT earlier shown in class – part of assigned reading & testable

## Slide 59: VM as a Tool for Memory Management - Sharing
Memory allocation
  Each virtual page can be mapped to any physical page
  A virtual page can be stored in different physical pages at different times
Sharing code and data among processes
  Map virtual pages to the same physical page (here: PP 6)
Virtual Address Space for Process 1:
Physical
Address
Space (DRAM)
0
N-1
(e.g., read-only
library code)
Virtual Address Space for Process 2:
VP 1
VP 2
...
0
N-1
VP 1
VP 2
...
PP 2
PP 6
PP 8
...
0
M-1
Address
translation
shown earlier in class – part of assigned reading & testable
Shown earlier in class – part of assigned reading & testable

## Slide 60: VM as a Tool for Memory Protection
Extend PTEs with permission bits
Page fault handler checks these before remapping
  If violated, send process SIGSEGV (segmentation fault)
Process i:
Address
READ
WRITE
PP 6
Yes
No
PP 4
Yes
Yes
PP 2
Yes
VP 0:
VP 1:
VP 2:
•
•
•
Process j:
Yes
SUP
No
No
Yes
Address
READ
WRITE
PP 9
Yes
No
PP 6
Yes
Yes
PP 11
Yes
Yes
SUP
No
Yes
No
VP 0:
VP 1:
VP 2:
Physical
Address Space
PP 2
PP 4
PP 6
PP 8
PP 9
PP 11
Review of earlier material – part of assigned reading & testable

## Slide 61: Simplifying Linking and Loading
Linking
  Each program has similar virtual address space
  Code, stack, and shared libraries always start at the same address
Loading
  execve() allocates virtual pages for .text and .data sections = creates PTEs marked as invalid
  The .text and .data sections are copied, page by page, on demand by the virtual memory system
Kernel virtual memory
Memory-mapped region for
shared libraries
Run-time heap
(created by malloc)
User stack
(created at runtime)
Unused
0
%esp
(stack
pointer)
Memory
invisible to
user code
brk
0xc0000000
0x08048000
0x40000000
Read/write segment
(.data, .bss)
Read-only segment
(.init, .text, .rodata)
Loaded
from
the
executable
file
NOT shown in class – NOT TESTABLE

## Slide 62: What does the VM layout look like?
4 GB address space
Text
Data
argv, envp
Heap
Stack
Text
Data
Interrupt stack
PT2
PT 1
NOT shown in class – NOT TESTABLE

## Slide 63: What does the VM layout look like in physical memory?
4 GB address space
Text
Data
argv, envp
Heap
Stack
Text
Data
Kernel Stack(s)
PT 1
Text
Data
argv, envp
Heap
Stack
PT 2
NOT shown in class – NOT TESTABLE

## Slide 64: OS Support: VIRTUAL MEMORY Summary
Each process has its own virtual address space
  machine instructions name memory with virtual addresses
  CPU hardware translates these to physical addresses using a page table
    called the memory management unit (MMU)
    page == disk block
    translation: VA = [ VPN ][ PAGE OFFSET] => PA = [ PFN ] [ PAGE OFFSET ]
  the base of the current process’s page table is stored in a reserved register for the MMU to use
Virtual Memory Mapping
  virtual address space is divided into a few large variable-size regions
  each VM region is a mapping of a file on the disk (or part of a file)
  mapping occurs
    the program text, global variables, libraries, stack and heap are mapped (to disk) when program starts
  physical memory is cache of this VM-mapped, disk-resident data
  implications for addressed-based naming

## Slide 65: Summary
Programmer’s view of virtual memory
  Each process has its own private linear address space
  Cannot be corrupted by other processes
System view of virtual memory
  Uses memory efficiently by caching virtual memory pages
    Efficient only because of locality
  Simplifies memory management and programming
  Simplifies protection by providing a convenient interpositioning point to check permissions

## Slide 66: Final Exam Format
2.5 hours (150 minutes) with format similar to quizzes but no group component
Expect 1 quiz+ worth of material since the last quiz (~40 minutes)
Remaining time for problems from the rest of the course material cover
Warning: unlike some courses material at the end of course doesn’t build directly on material from beginning of the course

## Slide 67: Broad Topic Reminder
Instruction sets – Assembly language
Pipelining
Caches
  Locality
File systems
Virtual Memory
Use the learning goals to direct your studying!

## Slide 68: Some Extra slides
The slides which follow were not shown in class, however we did talk about the material and did touch on it in earlier slides. As a result this is material you are responsible for. It is also covered in the assigned readings.
Some of the slides are repeats of earlier slides

## Slide 69: Virtual Memory
Initially assumed that processes had to be completely in memory to run
For the execution of any one instruction there are at most 3 distinct pages needed
  A code page (the next instruction, ignore deep pipelines)
  Data source (load)
  Data destination (store)
Programs exhibit a high degree of spatial locality
NOT shown in class – part of assigned reading & testable
Notes: 69
As a result only those pages actually need to be in physical memory
This works because most address references, be they to code, stack, or data areas, tend to exhibit a high degree of spatial locality
Also comment that that is why caches work
The most likely place to get data from is the same page you are currently on

## Slide 70: Virtual Memory - observations
Virtual memory allows multiple processes to run
Provides the illusion to the process that there is enough physical memory, even when there isn't
Allows better use of physical memory
  Only the memory that a process actually needs, needs be allocated; as opposed to what the process thinks it needs
Process "notifies" the OS that it needs a page by generating a fault – and the OS brings the page in, this is paging
NOT shown in class – part of assigned reading & testable
Notes: 70

## Slide 71: Demand Paging – big picture
Pages not in memory are marked as invalid
On fault check to see if the address is in the valid range for the process
  If not kill process
If page was allocated but not mapped in memory
  Find a free frame (may need to page something out)
  Add frame to page table
  Load frame from paging area or file system
NOT shown in class review of earlier material – part of assigned reading & testable
Notes: 71
The only time that a page needs to be in memory is when it is asked for
How does a page get asked for?
Previous models have the process killed if it accesses an invalid page
Key concept is that the fault is used to notify the OS that memory needs to be managed

## Slide 72: Paging Requirements
To support demand paging we need to:
  Know which process pages are valid
  Track page location
    Disk
    Memory
  Know which frames are free
Big question is what do we do when we run out of free frames?
NOT shown in class review of earlier material – part of assigned reading & testable
Notes: 72

## Slide 73: Page Replacement
The policy that selects the page frame to remove when space is needed
Poor page replacement algorithm can have a huge impact on the system performance
How do you decide what page to page out?
Notes: 73

## Slide 74: Replacement Policy
Optimal: This is the theoretical best possible choice
  The page to remove is the one that will not be used for the longest time (To implement this we would need to be able to predict the future)
FIFO:
  Keep a queue of pages, page that was brought in first gets selected
  Doesn't take advantage of spatial locality
Notes: 74

## Slide 75: Page Replacement - cont
LRU:
  Keep last used time for each page
  Select page with the oldest time stamp
  Impractical to implement
NOT shown in class review of earlier material – part of assigned reading &
testable for definitions
Notes: 75
When pushing a page remove it from its other location in the queue is there is one

## Slide 76: LRU approx:
Use page table reference bit
At a fixed interval shift reference bit into high bit of a counter for that page (counter is a history of the intervals each page was referenced in)
Page with smallest number is LRU (approximately)
  If all 1s then used in every scan interval, if all 0s then never used
Taled about in class
Notes: 76
Bit shifted in is 0

## Slide 77: Least Actively Used
Start page with activity of 3
During scan if reference bit set, increase activity count (max is 64), clear reference bit
If during scan reference bit clear, decrement activity count
When activity goes to 0 classify page as inactive.
NOT shown in class just need to know that it exists
Do not have to know how it is implemented
Notes: 77

## Slide 78: Page Replacement Considerations
78
Dirty pages are expensive to choose as one must copy them to disk and bring another page in (2 disk transfers)
Clean pages have only the page-in cost
Some pages can’t be paged out
Pages from low priority process should be freed before pages from higher priority processes
These points need to be considered in combination with the overall strategy such as LRU
NOT shown in class alluded to in other materials earlier in section
just need to know that it exists along with the types of information
That might be considered but not the details as to why or how that
Information would be used.
Notes: 78